Automated phase improvement
and model building
Kevin Cowtan
cowtan@ysbl.york.ac.uk

---
X-ray structure solution pipeline...
Data collection
Data
processing
Experimental
phasing
Molecular
Replacement
Density
Modification
Model
building
Refinement
Rebuilding
Validation

---
Density Modification
- Traditional density
  modification: e.g.
  'dm', 'solomon',
  'parrot', CNS
- Statistical density
  modification:
  e.g. 'resolve', 'pirate'

---
Density modification
Starting point:
- Structure factor amplitudes
- Phase estimates:
  - MR: Unimodel distribution
  - SAD: Biomodal distribution
I
I
MR
SAD
R
R

---
Density modification
How do we represent phase probability distributions?
- Phase/figure of merit - Φ, FOM
  - (unimodel, MR only)
- Henrickson-Lattman coeffs – ABCD
  - (bimodal or unimodal, general)
I
I
MR
SAD
R
R

---
Density modification
A,B represent a unimodal distribution (equivalent to Φ, FOM)
C,D represent the superimposed biomodality.
- Relative size and sign of A,B or C,D control the direction.
- Absolute size (A2+B2)½ controls the sharpness.
- For MR, we get A,B (or Φ, FOM) i.e. C=D=0.
- Together A,B,C,D can describe a bimodal distribution with any combination of peak height and direction.
I
I
A,B
Or Φ, FOM
C,D
R
R

---
Density modification
Density modification is a problem in combining information:

---
Density modification
1. Rudimentary calculation:
FFT
|F|, φ
ρ(x)
φ=φmod
Modify ρ
|Fmod|, φmod
ρmod(x)
FFT-1
Reciprocal space
Real space

---
Density modification
2. Phase weighting:
FFT
|F|, φ
ρ(x)
φ=f(φexp,φmod)
Modify ρ
|Fmod|, φmod
ρmod(x)
FFT-1
Reciprocal space
Real space

---
Density modification
3. Phase probability distributions:
centroid
FFT
|F|, P(φ)
|Fbest|, φbest
ρ(x)
P(φ)=Pexp(φ)×Pmod(φ)
Modify ρ
Pmod(φ)
|Fmod|, φmod
ρmod(x)
likelihood
FFT-1
Reciprocal space
Real space

---
Density modification
DM, SOLOMON, (CNS)
4. Bias reduction (gamma-correction):
centroid
FFT
|F|, P(φ)
|Fbest|, φbest
ρ(x)
Modify ρ
P(φ)=Pexp(φ)×Pmod(φ)
ρmod(x)
γ-correct
Pmod(φ)
|Fmod|, φmod
ργ(x)
likelihood
FFT-1
J.P.Abrahams

---
Density modification
PARROT
5. Maximum Likelihood H-L:
centroid
FFT
|F|, P(φ)
|Fbest|, φbest
ρ(x)
Modify ρ
ρmod(x)
γ-correct
|Fmod|, φmod
ργ(x)
MLHL
FFT-1

---
Density modification
RESOLVE, PIRATE
6. Statistical density modification:
centroid
FFT
|F|, P(φ)
|Fbest|, φbest
ρ(x)
P(φ)=Pexp(φ)×Pmod(φ)
Infer
Pmod(φ)
P(ρ(x))
Transform distribution
Reciprocal space
Real space

---
Density modification
Traditional density modification techniques:
- Solvent flattening
- Histogram matching
- Non-crystallographic symmetry (NCS) averaging

---
Solvent flattening

---
Histogram matching
P(r)
Noise
True
A technique from image processing for modifying the protein region.
- Noise maps have Gaussian histogram.
- Well phased maps have a skewed distribution: sharper peaks and bigger gaps.
Sharpen the protein density by a transform which matches the histogram of a well phased map.
Useful at better than 4A.
r

---
Non-crystallographic symmetry
- If the molecule has internal
  symmetry, we can average
  together related regions.
- In the averaged map, the
  signal-noise level is improved.
- If a full density modification
  calculation is performed,
  powerful phase relationships
  are formed.
- With 4-fold NCS, can phase
  from random!

---
Non-crystallographic symmetry
Crystallographic
Non-crystallograpic
Unaligned
2-fold
Aligned
2-fold
Aligned
6-fold
Aligned
5-fold

---
Non-crystallographic symmetry
Useful terms:
- Proper and improper NCS:
  (closed and open)
- Multi-domain averaging:
- Multi-crystal averaging:

---
Non-crystallographic symmetry
- How do you know if you have NCS?
  - Cell content analysis – how many monomers in ASU?
  - Self-rotation function.
  - Difference Pattersons (pseudo-translation only).
- How do you determine the NCS?
  - From heavy atoms.
  - From initial model building.
  - From molecular replacement.
  - From density MR (hard).
- Mask determined automatically.

---
Estimating phase probabilities
Problem: How do we go from a single phase estimate to a full phase probability distribution?
- We need to make an estimate of the error in the estimated phase.
- The errors in the phases are a parameter of the model itself, and may be estimated by likelihood methods.

---
Estimating phase probabilities
We know |Ftrue|, |Fpart|, fpart
Assuming fpart, fmiss are independent, then we expect the difference in magnitudes between |Ftrue| and |Fpart|, averaged over reflections, to give an indication of the phase error.

---
Estimating phase probabilities

---
Combining phase probabilities
Once we have an estimate for the error in fmod, we can construct a probability distribution Pmod(f).
The the next cycle can be started with
Pnew(f) = Pexp(f)Pmod(f)
Problem: Pexp(f) and Pmod(f) are not independent.
The result is bias, increasing with cycle.

---
Bias reduction
Solution:
Make each reflection only dependent on the other reflections in the diffraction pattern, and not on its own initial value.
Omit one reflection at a time, and use only the modified value of the omitted reflection. (Very slow.)
But can be implemented efficiently:
- Solvent flipping
- The g-correction

---
Density modification in Parrot
Builds on existing ideas:
- DM:
  - Solvent flattening
  - Histogram matching
  - NCS averaging
  - Perturbation gamma
- Solomon:
  - Gamma correction
  - Local variance solvent mask
  - Weighted averaging mask

---
Density modification in Parrot
New developments:
- MLHL phase combination
  - (as used in refinement: refmac, phenix.refine)
- Anisotropy correction
- Problem-specific density histograms
  - (rather than a standard library)
- Pairwise-weighted NCS averaging...

---
Estimating phase probabilities
Traditional approach: Rice likelihood function
Estimate the accuracy of the modified F/phase
Turn this into a phase probability distribution
Combine with the experimental phase probability
The estimate for the accuracy of the modified F/phase come from the agreement between the modified F and the observed F. Source of bias.

---
Estimating phase probabilities
Problem:
Error estimation does not take into account experimental phase information
The experimental data tells us that the probable error is different in the two cases
Using the additional information from the phases improves the error model and reduces bias.

---
Estimating phase probabilities
Solution:
MLHL-type likelihood
target function.
Perform the error estimation and phase combination in a single step, using a likelihood function which incorporates the experimental phase information as a prior.
This is the same MLHL-type like likelihood refinement target used in modern refinement software such as refmac or phenix.refine.

---
Recent Developments:
Pairwise-weighted NCS averaging:
- Average each pair of NCS related molecules separately with its own mask.
- Generalisation and automation of multi-domain averaging.
A
B
C
C
B
A
C
B
A

---
Parrot

---
Parrot
Summary:
A new classical density modification program, employing the latest techniques.
- Fully automated
- Fast
- Better results than DM

---
Density Modification
Kevin Cowtan, York.
Statistical density modification:
e.g. Resolve, Pirate

---
Density modification
- Traditional density modification:
  Take the phases to the mask.
  Use them to calculate a map.
  But how do we get back to:
  - reciprocal space?
  - probabilities?
- Statistical density modification:
  Take the mask to the phases.
  - First convert mask to
    probability.
  - Then transform that
    probability.

---
Statistical density modification
Form a statistical description of expected map features.
- e.g.
  - Protein has higher mean, and is more peaky (higher variance)
  - Solvent has lower mean, and is flatter (lower variance)

---
Statistical density modification
Probability of a map is determined by how well it fits these distributions:
Probable
Improbable

---
Statistical density modification
Probability of each structure factor is given by the probability of the corresponding map.
I (F(h))
R (F(h))

---
Statistical density modification
- Obtain per-grid density probability distributions.
- Transform to reciprocal space.
- Combine with experimental phases.
  - Map probability becomes phase probability distribution.
X
Improved phases
and maps.
Bricogne (1992) Proc. CCP4 Study Weekend
Bricogne (1997) Methods in Enzymology

---
Statistical density modification
Advantages:
- Reduced bias.
- Better phases.
Disadvantages:
- Slow.
- PIRATE in particular works well for some cases and badly for others.

---
Density Modification
Kevin Cowtan, York.
Some results...

---
DM vs Parrot
Map
correlations
Parrot:
No new
features
enabled.

---
Parrot: Rice vs MLHL
Map
correlations
Comparing
old and new
likelihood
functions.

---
Parrot: Isotropic vs Anisotropic
Map
correlations
Comparing
with and
without
anisotropy
correction.

---
Parrot: simple vs NCS averaged
Map
correlations
Comparing
with and
without
NCS
averaging.

---
Model Building
Model building software:
- Proteins:
  - Buccaneer
  - ARP/wARP
  - Phenix autobuild
- Nucleic acids:
  - Nautilus/Coot
  - ARP/wARP
  - Phenix autobuild

---
Buccaneer
The buccaneer software for automated model building of protein structures across a broad range of resolutions.
Kevin Cowtan
YSBL, University of York
cowtan@ysbl.york.ac.uk

---
Buccaneer: Method
Compare simulated map and known model to obtain likelihood target, then search for this target in the unknown map.
Reference structure:
Work structure:
LLK

---
Buccaneer: Method
Compile statistics for reference map in 4A sphere about Ca => LLK target.
Use mean/variance.
4A sphere about Ca also used by 'CAPRA'
Ioeger et al. (but different target function).

---
Buccaneer
Use a likelihood function based on conserved density features.
The same likelihood function is used several times. This makes the program very simple (<3000 lines), and the whole calculation works over a range of resolutions.
Finding, growing: Look for C-alpha environment
Sequencing: Look for C-beta environment
... x20
ALA
CYS
HIS
MET
THR

---
Buccaneer
10 stages:
- Find candidate C-alpha positions
- Grow them into chain fragments
- Join and merge the fragments, resolving branches
- Link nearby N and C terminii (if possible)
- Sequence the chains (i.e. dock sequence)
- Correct insertions/deletions
- Filter based on poor density
- NCS Rebuild to complete NCS copies of chains
- Prune any remaining clashing chains
- Rebuild side chains

---
Buccaneer
Case Study:
A difficult loop in a 2.9A map, calculated using real data from the JCSG.

---
Find candidate C-alpha positions

---
Grow into chain fragments

---
Join and merge chain fragments

---
Sequence the chains

---
Correct insertions/deletions

---
Prune any remaining clashing chains

---
Rebuild side chains

---
Comparison to the final model

---
Buccaneer
Model completion uses “Lateral growing”:
Grow sideways from existing chain fragments by looking for new C-alphas at an appropriate distance “sideways” from the existing chain:

---
Unmodeled density

---
Lateral growing likelihood function

---
New C-alpha candidates

---
Resulting model

---
Buccaneer: Results
Model completeness not very dependent on resolution:

---
Buccaneer: Results
Model completeness dependent on initial phases:

---
Buccaneer

---
Buccaneer
What you need to do afterwards:
- Tidy up with Coot.
  - Or ARP/wARP when resolution is good.
  - Buccaneer+ARP/wARP better+faster than ARP/wARP.
- Typical Coot steps:
  - Connect up any broken chains.
  - Use density fit and rotamer analysis to check rotamers.
  - Check Ramachandran, molprobity, etc.
  - Add waters, ligands, check un-modeled blobs..
  - Re-refine, examine difference maps.

---
Buccaneer: Summary
A simple, (i.e. MTZ and sequence), very fast method of model building which is robust against resolution.
User reports for structures down to 3.7A when phasing is good.
Results can be further improved by iterating with refinement in refmac (and in future, density modification).
Proven on real world problems.
Use it when resolution is poor or you are in a hurry. If resolution is good and phases are poor, then ARP/wARP may do better. Best approach: Run both!

---
Nucleic Acid Building
Nautilus:
- A new tool for nucleic acid model building
- Automated (CCP4i) or interactive (Coot)
- Starting from:
  - Experimental phasing
  - Molecular replacement
  - Protein complexes

---
Nautilus
The task:
- To build continuous nucleic acid chains into electron density.
- To assign sequence to those chains.
- To allow addition of nucleotide chains to non-nucleotide structures.

---
Nautilus
'Fingerprint' detection:
- Identify high and low density features consistent with the presence of nucleic acid features.
- Very fast.
- Related to 'Essens' (Kleywegt and Jones), but with looks at both ridges and troughs.

---
Nautilus
Types of fingerprint:
- Sugar
- Phosphate
- Base type (A/C/G/U)

---
Sugar:

---
Phosphate:

---
Nautilus
Use the difference between the mean of the 'high' points and the mean of the 'low' points as a score indicating how likely it is the given group is present at a given position and oriention.
Need to search positions and orientations – a more optimized version of the same target uses the minimum of the highs minus the maximum of the lows – can often stop the calculation before testing all the sample points.

---
Nautilus
Steps:
- Find chain seeds
- Grow into chains
- Join overlapping chains
- Link nearby chains
- Prune clashing chains
- Rebuild chains to ensure connectivity
- Assign sequence
- Build bases

---
Nautilus
Find:
- Optimised 6-d rotation-translation using the sugar or phosphate fingerprint.
  - ~5 seconds for whole ASU
- Sugar:
  - Build a single nucleic acid using the best matching equivalent from the database, scored by
    1 x sugar + 2 x phosphate fingerprints
- Phosphate:
  - Build a pair of nucleic acids using the best matching equivalent from the database, scored by
    1 x phosphate + 2 x sugar fingerprints

---
Nautilus
Grow:
- Try adding additional nucleic acids to either end of each fragment, scored by the sugar fingerprint and the intermediate phosphate fingerprint.
  - ~1-2 seconds
Join:
- Merge overlapping fragments into longer fragments
  - <0.1 second
Link:
- Join fragments with nearby 3' and 5' terminii
  - ~0.5 second

---
Nautilus
Prune:
- Eliminate clashing regions
  - <0.1 second
Rebuild chains:
- Rebuild each sugar-sugar link using a fragment from the database
  - ~0.3 seconds
Sequence:
- Score base-type fingerprints at each position and assign sequence
  - <0.1 second

---
Base:
Adenine-Uracil

---
Base:
Adenine-Uracil
U:O4
G:N2
U:O2

---
Nautilus
Adenine:
	U: / O4	U: / O2	G: / O6	G: / N1	G: / C2	G: / N2
A	-	-	+	+	+	-
C
G
U
G:O6
U:O4
G:N1
G:C2
G:N2
U:O2

---
Nautilus
Cytosine:
	U: / O4	U: / O2	G: / O6	G: / N1	G: / C2	G: / N2
A	-	-	+	+	+	-
C	+	+	-	-	-	-
G
U
G:O6
U:O4
G:N1
G:C2
G:N2
U:O2

---
Nautilus
Guanine:
	U: / O4	U: / O2	G: / O6	G: / N1	G: / C2	G: / N2
A	-	-	+	+	+	-
C	+	+	-	-	-	-
G	-	-	+	+	+	+
U
G:O6
U:O4
G:N1
G:C2
G:N2
U:O2

---
Nautilus
Guanine:
	U: / O4	U: / O2	G: / O6	G: / N1	G: / C2	G: / N2
A	-	-	+	+	+	-
C	+	+	-	-	-	-
G	-	-	+	+	+	+
U	+	+	-	-	-	-
G:O6
U:O4
G:N1
G:C2
G:N2
U:O2

---
Nautilus
But the real world isn't black and white. Ideally we want a probability of a base being of a particular type.
- Calculate z-scored densities for the density at each of the 6 sample positions for 200 bases (50 of each type), to form a sample database.
- Calculate z-scored densities for the 6 sample positions of the unknown base.
- Find the 50 closest matches to the unknown base from the database.
- Assign probability of being A/C/G/U on the basis of the proportion of of the 50 closest matches being of each type (+ an error term).
Google: k-NN (k-Nearest Neighbour)

---
Nautilus
A
G
A
C
U
?
?
G
C
U
A
G
?
C
?
C
U
G
A
U
?
A
G
C
U
A
?
C
U
A
G
C
?
A
G
C
C
U
U
G
?
G
A
C
C
U
U
G
?
C
U
G
A
U
?
C
U
A
G
C
C
G

---
A
G
Nautilus
C
G
A
C
U
U
U
?
C
U
A
G
A
A
?
?
C
U
G
A
C
C
?
A
G
C
U
G
G
?
C
U
A
G
G
G
?
A
G
C
C
U
U
U
U
?
G
A
C
C
U
U
C
C
?
C
U
G
A
C
C
?
C
U
A
G
G
G
✘

---
A
Nautilus
G
G
A
C
U
C
U
C
?
C
U
A
G
U
A
U
?
?
C
U
G
A
A
C
A
?
A
G
C
U
C
G
C
?
C
U
A
G
G
G
G
?
A
G
C
C
U
U
G
U
G
?
G
A
C
C
U
U
U
C
U
?
C
U
G
A
C
C
C
?
C
U
A
G
C
G
C
G
✘
✘

---
Nautilus
A
G
A
C
U
G
U
C
G
?
C
U
A
G
C
A
U
C
?
?
C
U
G
A
U
C
A
U
?
A
G
C
U
A
G
C
A
?
C
U
A
G
C
G
G
C
?
A
G
C
C
U
U
G
U
G
G
?
G
A
C
C
U
U
G
C
U
G
?
C
U
G
A
U
C
C
U
?
C
U
A
G
C
G
C
C
C
✘
✘
✔
G

---
Nautilus
G
A
C
U
A
U
C
G
A
?
C
U
A
G
G
A
U
C
G
?
?
C
U
G
A
C
C
A
U
C
?
A
G
C
U
U
G
C
A
U
?
C
U
A
G
A
G
G
C
A
?
A
G
C
C
U
U
C
U
G
G
C
?
G
A
C
C
U
U
G
C
U
G
G
?
C
U
G
A
G
C
C
U
G
?
C
U
A
G
U
G
C
C
U
C
✘
✘
✔
✘
C
G

---
Nautilus
Results:
- Good results on synthetic noisy data at 3.5A and user reports on real data at 3.8A.
  - Need more data
- Like 'buccaneer', phases are more important than resolution.
- Failed on a quadruplex structure with good phases.
  - Try a different database?

---
Achnowledgements
Help:
JCSG data archive: www.jcsg.org
Garib Murshudov, Raj Pannu, Pavol Skubak
Eleanor Dodson, Paul Emsley, Randy Read, Clemens Vonrhein
Funding:
The Royal Society, BBSRC